## Slide 1: Machine Learning for Pose Tracking using SLEAP
Maxwell Madden
Program in Neuroscience
University of Maryland School of Medicine

## Slide 2: Resources
sleap.ai – SLEAP Documentation/Website
github.com/talmolab/sleap – SLEAP code/github repo
Misc Video Processing Tools
Handbrake – a GUI for ffmpeg transcoding
ffmpeg – transcoding video
opencv – python video analysis
Tips
Console Commands

## Slide 3: Why SLEAP?
Open-source
Fast (around 5x the speed of DeepLabCut on equivalent datasets)
Requires smaller training sets for accurate pose-estimation
Highly configurable
SLEAP-Autoanalysis
Utility application for efficient ongoing analysis (cpu-inference)
Automatic transcoding prior to inference
Automatic framerate adjustment in cases of variable framerate or alignment with

## Slide 4: The SLEAP workflow

## Slide 5: Preparing our environments
Determine what computer(s) we will use
Install Anaconda/Miniconda
Install SLEAP
Install AutoSLEAP (Optional, includes ffmpeg)
conda create -y -n sleap -c conda-forge -c nvidia -c sleap -c anaconda sleap
conda create –y –n sleap-autoanalysis –c mxwllmadden –c conda-forge sleap-autoanalysis
Consider using a computer with a NVIDIA GPU for faster training/inference
Anaconda.com

## Slide 7
conda create -y -n sleap -c conda-forge -c nvidia -c sleap -c anaconda sleap
conda create –y –n sleap-autoanalysis –c mxwllmadden –c conda-forge sleap-autoanalysis
(Optional)

## Slide 8: Transcode video for input to SLEAP…
…via ffmpeg
…via the Autoanalysis Wizard
…via handbrake
(SLEAP-Autoanalysis) C:\Users\user> ffmpeg -y -i input.video -filter:v "fps=fps=30"
-c:v libx264 -pix_fmt yuv420p -preset superfast -crf 23 output.mp4
(SLEAP-Autoanalysis) C:\Users\user> autosleap wizard
SLEAP currently supports .mp4 or .avi
Occasionally video will be unplayable
due to corrupted headers/minor issues
This can sometimes be fixed by the
Transcoding process
Keep in mind that transcoding ALWAYS
results in quality loss. NEVER discard the original file.
www.handbrake.fr

## Slide 9: Label Images (Demo)

## Slide 10: Choose Hyperparameters
Feel free to experiment! Different
hyperparmaters may lead to better
performing models depending on
recording conditions/experiment etc

## Slide 12: Run SLEAP Training

## Slide 13: What is happening?
Calculate Loss
Batchsize = 2
Learning Rate
Learning
Algorithm
Batch size
Larger batch size increases training speed
at the cost of potentially reduced model
performance (overfitting)

## Slide 14: What is happening?
Epoch
Validation

## Slide 16: (Identify badly labeled frames)

## Slide 17: Run SLEAP Training again…
…and repeat until you have reliable tracking
You now have a model that can robustly track an animal in your behavioral arena/experiment
Models are only good at predicting pose
in situations they have been trained on…
Train a new model when
Camera position changes
Arena/experiment changes
sleap-convert --format analysis -o output.h5 input.predictions.slp
sleap-track input.mp4 –m training_config.json" --tracking.tracker none -o
output.predictions.slp --verbosity json --no-empty-frames

## Slide 18: Setup SLEAP-Autoanalysis
Most useful when running experiments over long periods on restricted hardware (cpu).
(SLEAP-Autoanalysis) C:\Users\user> autosleap new –f my_project
(SLEAP-Autoanalysis) C:\Users\user> autosleap run –f my_project

## Slide 19: SLEAP-Autoanalysis Settings

## Slide 20: Alternative: the Wizard
(SLEAP-Autoanalysis) C:\Users\user> autosleap wizard

## Slide 21: Framerate adjustment
Framerate in video is not guaranteed to be constant…
1 Second
File info:
Constant framerate
6 Hz
Trajectory Output:
Looks like we recorded
over 1.5 seconds of
movement!!!

## Slide 22: Framerate adjustment
1 Second
File info:
Constant framerate
6 Hz
Framerate adjusted for more accurate labeling!

## Slide 23: Opening and using the final output
import h5py
with h5py.File(filename, ‘r’) as file:
data = file[‘dataset’]
In python
In MATLAB
H5disp(filename);
data = h5read(filename, ‘dataset’);

## Slide 24: Labeling multiple, similar bodyparts
For difficult tracking tasks use of a Kalman filter can reduce errors (talk to steffan, likely requires high frame rate)

## Slide 25: Other capabilities of SLEAP
Labeling of multiple animals in the same arena
Tracking of skeletons, objects in arena
3d pose estimation via SLEAP-Anipose
github.com/talmolab/sleap-anipose

## Slide 26: Visualization
ALWAYS VISUALIZE YOUR DATA
import autosleap as asl
asl.visualize.label_video(
videofile.mp4,
trajectories.mp4, # non-adjusted
outputfile.mp4)
Tracking Visualization is available in the SLEAP GUI
As well as in the autosleap.visualize module

## Slide 27: Leveraging more powerful hardware
GPUs perform machine learning tasks at high speed.
Install the latest GPU driver from the
manufacturer website BEFORE setting
everything up
GPUs MUST be NVIDIA and have CUDA
support for use with SLEAP
Larger VRAM enables use of higher
resolution video or a larger batch size
hyperparameter
RTX GeForce 3060 currently offers 12GB VRAM for $300
Intel i5-12600K: 4 fr/sec
RTX GeForce 3070: 40 fr/sec